## Slide 1: MPI
Sapna Arora
Assistant Professor
PIET(ECE)

## Slide 2
1

## Slide 3
Addressing Modes of
8086

## Slide 4
The different ways in which a processor can access data are called
addressing modes.

## Slide 5: How 8086 accesses data?
8086 assembly language instructions can be used to illustrate the addressing modes
Format of MOV instruction
MOV destination, source

## Slide 6: Source of data can be
Immediate data
A specified register
A memory location specified in 1 of 24 different ways
Destination of data can be
  A specified register
A memory location specified in 1 of 24 different ways

## Slide 7: Classification of Addressing Modes
Immediate addressing mode
Direct addressing mode
Register addressing mode
Register Indirect addressing
mode
Indexed addressing mode
Register relative addressing mode
Based indexed addressing
mode
Relative based indexed addressing mode

## Slide 8: Immediate addressing mode
Immediate data is a part of instruction.
The immediate data may be 8-bit or 16-bit in size.
MOV AX, 0005H
In the above example, 0005H is the immediate data.

## Slide 9: Direct addressing mode
[5000H]
Memory Address (Offset) Is Directly Specified In The Instruction .
MOV AX,
Here, data besides in a memory location in the data segment.
Physical Address Of Memory Location Is Calculated
Using DS And Offset Value 5000H.

## Slide 10: Register addressing mode
Source/Destination Can Be One Of The 8086 Registers
Example:
MOV AX, BX ; 16-bit Data Transfer

## Slide 11: Register Indirect addressing mode
The Offset Address Of Data Is In Either BX Or SI Or DI Registers. The Default Segment Is Either DS Or ES.
Example: MOV AX, [BX].
Here, Data Is Present In A Memory Location In DS Whose Offset Address Is In BX.
The Effective Address Of The Data Is Given As 10H*DS+ [BX].

## Slide 12: Indexed addressing mode
MOV AX, [SI].
Here, data is available at an offset address stored in SI in DS.

## Slide 13: Register relative addressing mode
MOV Ax, 50H [BX].
Here, physical address is given as 10H*DS+50H+ [BX].

## Slide 14: Based indexed addressing mode
MOV AX, [BX] [SI].
Here, BX is the base register and SI is the index register. The physical address is computed as is the index register.
The physical address is computed as 10H*DS+[BX]+[SI].

## Slide 15: Relative based indexed addressing mode
50H [BX] [SI]
MOV AX,
Here, 50H is an immediate displacement, BX is a base register and SI is Here, 50H is an immediate displacement, BX is a base register and SI is an index register.
The physical address of data is computed as 10H*DS+
[BX] + [SI] + 50H.